## Slide 1
Survey of Reconfigurable Accelerator in Large-Scale Data Center and Cloud
Project Presentation of CSC6031: Advanced Computer Architecture
● Presenter: Liu Yuxuan
Email: yuxuanliu1@link.cuhk.edu.cn
The Chinese University of Hong Kong, Shenzhen

## Slide 2
CONTENTS
01
Introduction to Reconfigurable Accelerator and FPGA
02
Applying FPGAs in Large-Scale Data Center
Case Study of Microsoft Project Catapult
03
Challenges and Opportunities of FPGAs in the Cloud
04
Conclusion

## Slide 3
01
PART
Reconfigurable Accelerator and FPGA
  Introduction, Background, and Motivation

## Slide 4
What is Reconfigurable Accelerator?
Background: Slowing of Moore’s Law
  Domain-Specific Architecture (DSA) as a desperate way for further speedup
  Seeks further performance and energy gain by sacrificing homogeneous to heterogeneous
    Switch from architecture-dominant to application-dominant
Three Major Types of DSA
  Graphics Processing Unit (GPU)
  Reconfigurable Accelerator (FPGA)
  Application-Specific Integrated Circuits (ASIC)

## Slide 5
What is FPGA?
Field Programming Gateway Array
  Programmable logic blocks and interconnects that can reconfigure after manufacture
  Logic blocks contain look-up tables (LUTs), flip-flops that can implement logic functions
Fig.2 Simplified Example of a Logic Cell
Fig.1 General FPGA Architecture

## Slide 6
Why FPGA? — Market and Players
Huge Size & Growth in FPGA Market
  6.5 billion USD global FPGA market
  48% Compound Annual Growth Rate (CAGR) between 2020 and 2027
  Serves over 1 million hosts for Microsoft Azure SmartNICs application
Major FPGA Service Providers
  Microsoft (Project Catapult, Brainwave, and Azure SmartNICs)
  Amazon Web Services (AWS) EC2 F1
Major FPGA Manufacturers
  Xilinx (Acquired by AMD in 2022)
  Altera (Acquired by Intel in 2015)
Straix IV FPGA from Altera
Spartan FPGA from Xilinx

## Slide 7
Why FPGA? — Flexibility-Efficiency Trade-Off
Good Balance Between Flexibility and Efficiency
  Flexibility: Reconfigurability means lower non-recurrent expense (NRE) and faster deployment
    Alibaba has reported 75% savings in TCO by using FPGAs to oversee product images on its e-commerce site.
  Efficiency: Higher throughput than CPU, more energy efficient and lower latency than GPU
Fig.3 Trade-Off between Flexibility and Efficiency
FPGA Here

## Slide 8
Why FPGA? — A Closer Look at Performance
Compared with CPU
Catapult on Bing’s Web Search Ranking Application
  95% more throughput with the same latency
  29% lower latency under the same throughput
Compared with GPU
Catapult on Image Classification
  90% power save
  remain 40% to 50% peak throughput
Fig.5 Comparison of Image Classification Throughput and Power Consumption
FPGA
GPU
Fig.4 Throughput and Latency Comparison for Web Search Ranking

## Slide 9
02
PART
FPGAs in Large Scale Data Center
  Case Study of Microsoft Project Catapult
  Align with Textbook Chapter 7.5

## Slide 10
Milestone of Microsoft Project Catapult
2010
2014
2011
Proposal Initiate
Release Catapult v1 ISCA’14
First Prototype Developed
Catapult v0 accelerating Bing IndexServer Engine
Deploy on 1632 servers accelerating web search services
2016
Release Catapult v2 MICRO’16
Deploy on 5760 servers accelerating major web search and network services
Propose to use FPGAs at scale to accelerate web search
2018
Release Brainwave ISCA’18
Use FPGAs to accelerate DNN and SmartNICs

## Slide 11
Catapult v0 — Straightforward But Poor Design
Motivation & Goal
  Achieve the required capacity for a large-scale reconfigurable fabric
Six-in-One Board Design
  Six Xilinx Virtix-6 FPGA on one daughter board
  FPGAs inter-connected in a mesh network with general-purpose I/Os
  FPGA serves as local compute accelerator (co-processor)
Problems
  Inelastic FPGA Resources
  Incompatible power and physical space for the board
  Single-Point-Of-Failure
  Limited Functionality of local co-processor architecture
Fig 6. Photograph of Catapult v0 Board

## Slide 12
Catapult v1 — A Global View
Motivation & Goal
  Elastic, low-latency, and good failure detection & recovery
One-in-One Board Design
  One Altera Straix V FPGA on one daughtercard with 8GB DRAM
  Inter-FPGA direct secondary network in 2D 6x8 torus (48 as a rack)
  FPGA serves as local and remote compute accelerator (co-processor)
    Use one local FPGA through PCIe
    Use remote FPGAs with secondary network
Cost & Power Consumption
  Less than 30% extra system TCO
  Less than 10% extra server power
Fig 8. Diagram of 1U, half-width server hosting the FPGA board
Fig 7. 2D 6 x 8 Torus Network Topology
FPGA Here

## Slide 13
Catapult v1 — Shell & Role Architecture
Motivation
  A simple and accessible interface to software application
    Enhance user productivity and design re-use
    Resilience and debugging support
Partial Reconfiguration with Shell/Role Architecture
  Split all programmable logic blocks into shell & role
  Shell (23%): reusable common logic across application
    Not configurable logics by the application
  Role (77%): Acceleration Application logic itself
    Configurable logics by the application
Fig 8. Shell & Role Architecture for Catapult v1

## Slide 14
Catapult v1 — Accelerate Bing Ranking Service
Macro-pipeline with Multiple FPGA
  1 FPGA for Feature Extraction (FE)
  2 FPGAs for Free-Form Expressions (FFE)
  1 FPGA for Compression
  3 FPGAs for Machine-Learning Scoring Models
  1 FPGA for redundancy in case of failure
Some Useful Terms for Later Understanding
  <Query, Document> pair as input request
    Query: user-input keywords for searching
    Document: web pages, files or videos
  Free-Form Expression
    Combine multiple extracted features to be a hybrid feature
Fig 9. Roles of FPGAs on the Reconfigurable Fabric

## Slide 15
Catapult v1 — Accelerate Feature Extraction with MISD
Why MISD for FE?
  Need to compute thousands of different features
  of the same document, which is read-only in this stage
  Multiple operations performed on the same data
  Different feature needs different computation, hard to SIMD parallelism
  Multi-threading is not needed as the document is shared and read-only, energy in-efficiency BTW
How MISD performs parallelism?
  43 unique FE state machines in parallel on one document
  Merge similar computations in one state machine for better throughput
  Gather feature values from feature extraction state machines
Fig 9. MISD Parallelism with FSMs

## Slide 16
Catapult v1 — Accelerate FFE with Thread-Interleaving
Why Multi-Threading for FFE?
  Highly varied complexity of expressions
    Highly varied latency From simple add to complex
  Massive multi-thread interleaving can hide the long latencies of operations
How FFE gets accelerated?
  Dedicated function units like
  60 cores x 4 threads Interleaving on one single FPGA
  Static thread scheduling for determined performance
  Double-buffered feature storage for higher throughput
    Enable one to be loaded while another being processed
Fig 10. FFE Placed-and-Routed on FPGA

## Slide 17
Catapult v1 — Putting it All Together
How FPGA Succeed in Accelerating Ranking Service
  Reconfigure Different Architecture for Different Tasks
  Dedicated function units for complex operations
  Dedicated secondary network between FPGAs
Problems on Secondary Network
  Expensive and complicated secondary network, hard to maintain
  One node failure in torus network affects the neighbor nodes and requires re-routing
  Dedicated secondary network is hard to scale for more FPGAs inter-connected
  Back-end Cloud Architecture limits the functionality of other areas like networking and storage
Fig 11. 2D 6 x 8 Torus Network Failure

## Slide 18
Break — Review of Cloud Acceleration Architectures
Four Types of Cloud Acceleration Architectures Mentioned in this Survey
  Co-Processor (Catapult v0): Local Compute Acceleration
  Back-End (Catapult v1): ultra-low latency, rack-scale FPGA-FPGA Connection
  Bump-in-the-Wire (Catapult v2 & Brainwave): large scale compute (local and remote), network, and storage acceleration
  Smart NICs (Azure NSDI’18): SDN & local network acceleration
Fig 12. Four Cloud Acceleration Architectures in this Survey

## Slide 19
Catapult v2 — Bump-in-the-Wire Cloud Architecture
Motivation
  Enable FPGAs to accelerate more tasks
    Local & Remote Compute Acceleration
    SDN and Network Crypto
  More Scalable and Resilient to Failure
Hardware Plane & Design
  FPGA as a layer between server’s NIC and the Ethernet network switches
  FPGAs can generate and consume their own network flow independent of the host CPU (Pure FPGA-FPGA Connection)
Fig 13. (a) Decoupled Programmable Hardware Plane
(b) Server + FPGA Schematic

## Slide 20
Catapult v2 — New Shell & Role Architecture
Compared to Catapult v1
  Large area as network layer (occupies 14% area)
  Shell occupies more area than v1 (23% to 44%)
  Enable Multiple Roles in one FPGA
FPGA as a Global Resource Pool
  Light-weight Transport Layer (LTL) is the protocol of FPGA-FPGA inter-connection through primary network.
    Comparable round-trip latency as torus (2.9 for L0 tier)
  Intra-FPGA Elastic Router (ER) with virtual channel support for multi-roles.
  All FPGAs form a elastic and scalable resource pool
Fig 14. Shell & Role Architecture on Catapult v2

## Slide 21
Catapult v2 — New Acceleration Possibilities
Local Compute Accelerations
  Intra-FPGA (Multi-Role) Connection with Elastic Router (ER)
  CPU-FPGA connection through PCIe bus (ER as Intermediate Router)
Remote Compute Accelerations
  Inter-FPGA connection with LTL through high bandwidth (40Gb/s) primary network
    Elasticity: Spare FPGAs can be donated and Services can allocate more than 1 FPGAs for acceleration
Local Network Acceleration
  Offload encrypt/decrypt workload from CPU to bump-in-the-wire FPGA
  AES-CBC-SHA1 crypto needs at least 15 CPU cores for 40 Gb/s full duplex
  Acceptable higher FPGA latency than CPU (11 over 4 ), much better performance in GCM crypto
  Also deployed for Azure software-define networks (SDN)

## Slide 22
Catapult v2 — Hardware-as-a-Service (HaaS)
Multi-Level Resource Manager
  From top to bottom
    Resource Manager (RM)
    Service Manager (SM) as one of FM nodes in a service
    FPGA Manager (FM)
Go from Data Center to Cloud
  Catapult v1 (ISCA’14): A Reconfigurable Fabric for Accelerating Large-Scale Datacenter Services
  Catapult v2 (MICRO’16): A Cloud-Scale Acceleration Architecture
  More elastic, scalable, failure resilience, and easy-to-share
Fig 15. Two HaaS-Enabled Accelerator Services

## Slide 23
Catapult v2 — Putting it All Together
Features over Catapult v1
  Bump-in-the-wire instead of back-end architecture
  Able to take and accelerate more workloads
  inter/intra FPGA connection without secondary network
  Cloud-Scale elastic, scalable and easy-to-share solution
Better Performance over Software Solution
  2.25x more throughput
  20% tail latency drop in both local & remote acceleration
Problems
  Too much FPGA area occupied by shell
  Lack of multi-tenant resource sharing as a cloud service provider
Fig 16. Latency and Throughput for Catapult v2

## Slide 24
Catapult to Brainwave — AI Acceleration
Background & Motivation
  Accelerate NN inference based on Catapult v2 FPGA infrastructure
  GPUs have excellent performance with batching but long latency
    parallelism within and across request
    under-utilization and long latency for online mode, when requests come one by one
  Exploit parallelism within single request for real-time, low-latency AI
Trade-Off: Faster Clock Rate vs. Higher Utilization
  Increasing clock rate improves performance, but reduce efficiency
    Increased pipeline bubbles
  FPGAs have lower clock rate than GPU and ASIC due to the overhead of reconfigurable logic (from performance-dominant to efficiency-dominant)
Fig 17. Utilization scaling with
increasing batch size
GPU
FPGA

## Slide 25
Brainwave — NPU + FPGA Architecture
Single-Thread SIMD Microarchitecture
  Only one technique is tied to FPGA while others could stay in NPU
  Focus on parallelizing matrix-vector multiplication
  Chaining of Dependent Instructions
    Pass values directly from one operation to the next
    Avoid complex dependency check and multi-port register file
  Mega-SIMD with 2D Tiled Matrix
Configurable NPU ISA with Compact and Simple Abstraction
  Variable data types (precision, fp8, fp16, fp32, etc)
  Variable vector size & matrix-vector tile size
Evaluation
  35 TFLOPS on large RNN benchmarks without batching
  10-90x lower latency than GPGPU for large models
Fig 18. Overview of Matrix-Vector Tile Engine

## Slide 26
Catapult — Summary
Analysis on the 5 Guidelines of DSA proposed by our Textbook
  Use dedicated memories to minimize the distance over which data is moved
    There are on-chip memory in FPGA, that can be customized for application use
  Invest the resources saved from dropping advanced microarchitectural optimizations into more arithmetic units or bigger memory
    One Altera V FPGA has 3926 18-bit ALUs. Also, the 60 cores can be created on one FPGA for FFE acceleration
  Use the easiest form of parallelism that matches the domain
    MISD for FE Acceleration and multi-thread interleaving for FFE acceleration
  Reduce data size and type to the simplest needed for the domain
    Brainwave NPU supports various data types, like fp8, fp16, fp32, etc.
  Use a domain-specific programming language to port code to the DSA
    Microsoft still uses Verilog HDL to implement its FPGA accelerator

## Slide 27
03
PART
Challenges of FPGAs in the Cloud
  Quick Review of Related Area and Works

## Slide 28
Enabling FPGAs in the Cloud
Like VMs, FPGA cloud service providers must allow multi-tenant applications running on the same FPGA with the following constraints
Resource Abstraction
  FPGAs as programmable resource pool (PRP)
  Abstracted into resources of registers, LUTs, memory, etc
  Need HW manufacturer to support HW-independent bitfiles
FPGA Sharing
  virtualization and isolation among tenants applications
  AmorphOS and Coyate OS Abstraction working on this topic
Compatibility
  Unified Software-Hardware Interfaces
Security
  Prevent one application crashing the whole system
  Prevent applications to steal or pollute other’s memory data
Fig 17. FPGA Framework in a Cloud

## Slide 29
Techniques to Simplify FPGA Programming
Why FPGA is so hard to program?
  Register Transfer Level (RTL) programming
  completely different programming paradigm with SW languages
Compiler Support
  Intel High-Level Synthesis (HLS) compiler
    Takes untimed C++ codes and generates production-quality RTL code optimized for Intel FPGA. Accelerate the verification time over RTL.
  Common Compiler Backend
    Optimize Abstract Syntax Tree (AST) and generate suitable C++ for HLS
  Automated Binary Translation from SW to HW
    Translate ARMv8, RISC-V32imaf ISAs to HDL
Fig 18. A Verilog Code Snippet

## Slide 30
Conclusion
Great Potential of Reconfigurable Accelerator in Data Center and Cloud
  Development of domain-specific architecture as another way than general-purpose architecture
  Trend of accelerating all kinds of applications with cloud infrastructure (Alibaba Damo Academy)
  Host the most suitable DSA for the specific application (web search ranking, network, DNN, etc)
  Comparable performance with lower memory consumption and better resource utilization
Challenges & Opportunities
  Resource abstraction & sharing for multi-tenant applications on the same FPGA like VM
  Complexity of HDL Programming (HLS compiler support, binary translation)
Interesting Trade-Offs
  homogeneous vs. heterogeneous and specialization
  high clock rate vs. high resource utilization (fewer pipeline bubbles)

## Slide 31
References
Putnam, Andrew, et al. "A reconfigurable fabric for accelerating large-scale datacenter services." 2014 ACM/IEEE 41st International Symposium on Computer Architecture (ISCA). IEEE Computer Society, 2014.
Caulfield, Adrian M., et al. "A cloud-scale acceleration architecture." 2016 49th Annual IEEE/ACM international symposium on microarchitecture (MICRO). IEEE, 2016.
Fowers, Jeremy, et al. "A configurable cloud-scale DNN processor for real-time AI." 2018 ACM/IEEE 45th Annual International Symposium on Computer Architecture (ISCA). IEEE, 2018.
Firestone, Daniel, et al. "Azure Accelerated Networking:{SmartNICs} in the Public Cloud." 15th USENIX Symposium on Networked Systems Design and Implementation (NSDI 18). 2018.
Hennessy, John L., and David A. Patterson. Computer architecture: a quantitative approach. Elsevier, 2011.
Shahzad, Hafsah, Ahmed Sanaullah, and Martin Herbordt. "Survey and future trends for FPGA cloud architectures." 2021 IEEE High Performance Extreme Computing Conference (HPEC). IEEE, 2021.
Ovtcharov, Kalin, et al. "Accelerating deep convolutional neural networks using specialized hardware." Microsoft Research Whitepaper 2.11 (2015): 1-4.
Skliarova, Iouliia, and Valery Sklyarov. FPGA-BASED hardware accelerators. Springer International Publishing, 2019.

## Slide 32
References
Chen, Fei, et al. "Enabling FPGAs in the cloud." Proceedings of the 11th ACM Conference on Computing Frontiers. 2014.
Rankin, Dylan, et al. "FPGAs-as-a-service toolkit (FaaST)." 2020 IEEE/ACM International Workshop on Heterogeneous High-performance Reconfigurable Computing (H2RC). IEEE, 2020.
Khawaja, Ahmed, et al. "Sharing, Protection, and Compatibility for Reconfigurable Fabric with {AmorphOS}." 13th USENIX Symposium on Operating Systems Design and Implementation (OSDI 18). 2018.
Korolija, Dario, Timothy Roscoe, and Gustavo Alonso. "Do {OS} abstractions make sense on {FPGAs}?." 14th USENIX Symposium on Operating Systems Design and Implementation (OSDI 20). 2020.
Cong, Jason, et al. "FPGA HLS today: Successes, challenges, and opportunities." ACM Transactions on Reconfigurable Technology and Systems (TRETS) 15.4 (2022): 1-42.
Del Sozzo, Emanuele, et al. "A common backend for hardware acceleration on FPGA." 2017 IEEE International Conference on Computer Design (ICCD). IEEE, 2017.
Paulino, Nuno, et al. "A Binary Translation Framework for Automated Hardware Generation." IEEE Micro 41.4 (2021): 15-23.

## Slide 33
Thanks for Listening!
Q&A Session